## Slide 1
XLR8
Design and Implementation of a
ShuffleNet V2 Accelerator
using RTL and HLS
Graduation Project Discussion | Faculty of Engineering
Academic Year 2025 â€“ 2026
Target : Xilinx Zynq UltraScale+ ZU19EG

## Slide 2
What We Built
1,216
fps throughput
78.76%
DSP utilization
6.426 W
total power
0.00529 J
energy per frame
+0.125 ns
WNS â€” timing closed
29x
more efficient than HLS
One custom FPGA accelerator. ShuffleNet V2. Zynq UltraScale+ ZU19EG.

## Slide 3
Team XLR8
Graduation Project Members â€” 2025 / 2026
1
[ PHOTO ]
Ahmed Ahmed Nageeb Ahmed Elbermawy
RTL Architecture & Project Lead
2
[ PHOTO ]
Yousef Abdulrahman Abdulnabi Abdulrahman
HLS Design & Verification
3
[ PHOTO ]
Mohamed Ahmed Roshdy Saad
Software Model & Toolchain
4
[ PHOTO ]
Basmala Hatem Abdullah Mostafa
Documentation & Analysis
"Speed is our design principle."

## Slide 4
Presentation Outline
What we will cover today
Act I â€” Introduction & Design
1. The Edge AI Challenge
2. Our Platform & Model
3. Q6.8 Quantization
4. Hardware Architecture
5. Verification
Act II â€” Results & Conclusion
6. Synthesis Results
7. RTL vs HLS Comparison
8. Hardware Demo
9. Conclusion
10. Q&A

## Slide 5
ACT
1
INTRODUCTION & DESIGN JOURNEY
From the first transistor to real-time AI inference on FPGA

## Slide 6
01
The Edge AI Challenge
Why cloud AI fails at the edge â€” and what it takes to fix it
XLR8

## Slide 7
1.1
VLSI + AI: 60 Years of Convergence
Two independent revolutions that collided in the 2010s
â–¸ 1958 â€” Jack Kilby invents the IC: 6 transistors on germanium
â–¸ Moore's Law (1965): transistor count doubles every ~18 months
â–¸ 2023 â€” Apple M3: 19 billion transistors on a single chip
â–¸ 1957 â€” Rosenblatt's Perceptron: the first artificial neuron
â–¸ 2012 â€” AlexNet wins ImageNet with a GPU: the AI breakthrough moment
â–¸ Today â€” AI compute demand grows 10Ã— per year; hardware barely keeps up
â–¸ The answer is custom hardware â€” FPGAs are the programmable path to it
[ INSERT FIGURE ]
VLSI + AI dual timeline Line chart (log scale Y): transistor count 1971â€“2023 with chip labels (Intel 4004, Core2, Apple M3). Green diamond markers for AI milestones: Perceptron (1957), Backprop (1986), AlexNet (2012), Transformer (2017), LLMs (2023). Era shading for SSI/MSI/LSI/VLSI/ULSI.

## Slide 8
1.2
Power vs. Performance â€” The Edge AI Constraint
Cloud GPUs are overkill. Embedded ARM is too slow. FPGAs hit the sweet spot.
[ INSERT FIGURE ]
Scatter plot (log-log): Power (W) vs Throughput (fps). Points: ARM A53 (gray), Jetson NX (blue), GTX 1080 (gray), Our FPGA ZU19EG (green, highlighted with white border). Diagonal dashed lines for 10/100/1000 fps/W efficiency. Shows FPGA wins the throughput-per-watt tradeoff.

## Slide 9
1.3
Why Cloud AI Fails at the Edge
The embedded edge demands intelligence without the infrastructure
â–¸ Latency: 50â€“500 ms round trip â€” useless for real-time control or robotics
â–¸ Privacy: raw video leaves the device and travels the internet
â–¸ Bandwidth: streaming HD to the cloud consumes significant network resources
â–¸ Reliability: no connectivity = no AI â€” fails in tunnels, remote sites, factories
â–¸ Power: a data-center GPU draws 300 W â€” impossible on a battery or embedded rail
â–¸ Edge AI â€” run the model locally, on the device itself:
â€¢ Sub-millisecond latency â€” data stays on device â€” works offline
â€¢ Requires a power budget of watts, not kilowatts
â–¸ Our solution: ShuffleNet V2 on Zynq UltraScale+ ZU19EG â€” 1,216 fps at 6.426 W

## Slide 10
02
Platform & Model
Choosing the right hardware and the right neural network
XLR8

## Slide 11
2.1
Our Platform â€” iWave ZU19EG SoC
ARM PS runs Linux and controls the system. Custom PL runs ShuffleNet at 100 MHz.
[ INSERT FIGURE ]
ZU19EG block diagram Two nested rectangles: PS (left, blue border) containing ARM Cortex-A53 x4, DDR4, USB/GigE/UART, AXI Interconnect, Linux label. PL (right, green border) containing MMCM 100 MHz, AXI4-Lite Slave, ShuffleNet V2 Accelerator (Group1+2+3), resource count row (522K LUTs | 1,968 DSPs | 984 BRAM36K). Horizontal AXI arrow between PS and PL.

## Slide 12
2.2
Why ShuffleNet V2?
â–¸ ShuffleNet V2 x1.0 (Ma et al., ECCV 2018) â€” designed for hardware efficiency:
â€¢ 146 M MACs per 224Ã—224 image â€” lowest among competitive CNNs
â€¢ 71.8% Top-1 accuracy on ImageNet (PyTorch pretrained)
â€¢ 2.3 M parameters â€” fits entirely in on-chip BRAM
â–¸ Why it maps perfectly to FPGA hardware:
â€¢ Equal channel widths minimize memory access cost (analytically proven)
â€¢ Depthwise separable convolutions map directly to our parallel filter units
â€¢ No batch normalization at inference (folded into weights) â€” simpler hardware
â€¢ Avoids element-wise add â€” uses concat instead (cheaper on FPGA)
â–¸ Full pipeline: Conv1 â†’ MaxPool â†’ 16 Shuffle Blocks â†’ Conv5 â†’ AvgPool â†’ FC â†’ Top-1
[ INSERT FIGURE ]
ShuffleNet V2 full architecture diagram Horizontal flow: Input box â†’ Conv3Ã—3 + MaxPool (GROUP 1, blue bracket) â†’ Stage 2 (4 blocks, 24â†’116 ch) + Stage 3 (8 blocks) + Stage 4 (4 blocks, â†’464 ch) (GROUP 2, green bracket) â†’ Conv5 + AvgPool+FC (GROUP 3, purple bracket) â†’ class output. Channel dimension annotations above each stage.

## Slide 13
2.3
ShuffleNet V2 â€” Architecture Overview
3 hardware groups processing 3 different images concurrently
[ INSERT FIGURE ]
ShuffleNet V2 full architecture diagram (same as slide 2.2 but full-width version) Horizontal flow: Input â†’ Conv3Ã—3/MaxPool (Group 1, blue) â†’ 3 stages of shuffle blocks (Group 2, green) â†’ Conv5/AvgPool/FC (Group 3, purple) â†’ class 0-999. Include feature map dimension labels (56Ã—56, 28Ã—28, 14Ã—14, 7Ã—7) above each stage.

## Slide 14
2.4
Computational Profile â€” Where the MACs Live
â–¸ 146 M total MACs per inference â€” distributed across all layers:
â€¢ Conv1 (3Ã—3): 43 M MACs â€” 24 parallel filter units process this stage
â€¢ Stage 2â€“4 (DW+PW): 72 M MACs â€” 58 parallel DW + 58 parallel PW filter units
â€¢ Conv5 + AvgPool + FC: 24 M MACs â€” Group 3, the pipeline bottleneck
â–¸ Group 3 (822 Î¼s) is the bottleneck â€” pipeline throughput = 1/822Î¼s = 1,216 fps
â–¸ All hardware parallelism decisions flow from this analysis
[ INSERT FIGURE ]
MAC count horizontal bar chart Bars (horizontal): Conv1 (3Ã—3) = 43M GREEN, MaxPool = 0.8M gray, Stage2 DW+PW = 33M blue, Stage3 DW+PW = 38M blue, Stage4 DW+PW = 21M blue, Conv5 = 23M blue, FC = 1M gray. X-axis: MACs (millions). Title: "Computational Load per Layer â€” 146M total MACs".

## Slide 15
03
Q6.8 Quantization
Turning floating-point weights into pure integers
XLR8

## Slide 16
3.1
Q6.8 Fixed-Point Format
15-bit signed: 1 sign + 6 integer + 8 fractional bits. No floating-point hardware needed.
[ INSERT FIGURE ]
Q6.8 bit-field diagram 15 equal-width boxes in a row, labelled S, 5, 4, 3, 2, 1, 0, -1, -2, -3, -4, -5, -6, -7, -8. Colors: S=black, bits 14-8 (integer)=blue, bits 7-0 (fractional)=green. Bit position numbers below each box (14 down to 0). Below: three double-headed arrows spanning Sign / 6-bit Integer / 8-bit Fractional with labels. Top text: "Q6.8 Fixed-Point Format â€” 15-bit signed (1+6+8)" and example: 3.14 â†’ 803 â†’ 803/256 = 3.137.

## Slide 17
3.2
The Quantization Pipeline
PyTorch â†’ BN-folding â†’ Q6.8 quantization â†’ bit-true Python â†’ RTL-ready hex weights
â–¸ Step 1 â€” Load pretrained weights from PyTorch (float32, 71.8% Top-1)
â–¸ Step 2 â€” Batch Normalization Folding:
â€¢ Absorb BN scale/shift into preceding Conv: w' = wÃ—(Î³/Ïƒ), b' = (bâˆ’Î¼)Ã—(Î³/Ïƒ)+Î²
â€¢ Result: only Conv + ReLU remain â€” no BN hardware needed at all
â–¸ Step 3 â€” Q6.8 quantization: multiply by 256, round, clamp to 15-bit
â–¸ Step 4 â€” Build a bit-true Python model that mirrors exact hardware arithmetic:
â€¢ Integer MACs, right-shift accumulation, saturating clamping, ReLU
â€¢ 3 arithmetic bugs found and fixed during development (see Q&A backup slides)
â–¸ Step 5 â€” Accuracy validation: ~71% Top-1 retained after quantization
â–¸ Step 6 â€” Export weights as .hex files â†’ $readmemh â†’ synthesized BRAMs and ROMs
â–¸ Per-layer bit-width optimization: G1=12-bit, G2-DW=15-bit, G2-PW=11-bit, FC=9-bit

## Slide 18
04
Hardware Architecture
50 modules, 48 testbenches, 1 silicon result
XLR8

## Slide 19
4.1
3-Group Pipelined Architecture
Group 1, 2, and 3 run concurrently on 3 different frames at all times
[ INSERT FIGURE ]
3-group pipeline block diagram Horizontal flow (left to right): ARM PS box â†’ AXI4-Lite block â†’ Photo BRAM (ping-pong) â†’ GROUP 1 box (Conv3Ã—3 + MaxPool, blue, larger) â†’ Maxpool BRAM â†’ GROUP 2 box (16 Shuffle Blocks, green, larger). GROUP 3 (AvgPool+FC, purple) is positioned BELOW GROUP 2 with a downward arrow. Arrow from GROUP 3 to class output box. Frame labels above/beside each group: "Frame N" (G1), "Frame N-1" (G2), "Frame N-2" (G3).

## Slide 20
4.2
Pipeline Timing â€” How 1,216 fps is Achieved
G3 at 822 us is the bottleneck. Pipeline throughput = 1/822 us = 1,216 fps.
[ INSERT FIGURE ]
Gantt chart (horizontal bar chart) Three rows: Group 3 AvgPool+FC (purple), Group 2 Shuffle Blocks (green), Group 1 Conv+MaxPool (blue). Each row shows Frame 1, Frame 2, Frame 3 bars. A vertical green dashed line at x=0.822 ms labelled "Pipeline period = 0.822 ms â†’ 1,216 fps" positioned between Group 1 and Group 2 rows. Right-side latency labels: 0.822 ms â† bottleneck, 0.798 ms, 0.633 ms. X-axis: Time (ms) 0 to 4.2.

## Slide 21
4.3
The Shuffle Block â€” Our Key Design Decision
â–¸ Each of the 16 shuffle blocks in Group 2 processes one stage of the network
â–¸ Full ShuffleNet V2: Branch 2 runs PW1Ã—1 â†’ DW3Ã—3 â†’ PW2Ã—1 (3 sequential convolutions)
â–¸ Our RTL design â€” a deliberate architectural choice:
â€¢ DW3Ã—3 âˆ¥ PW1Ã—1 â€” both run simultaneously as a single parallel stage
â–¸ Why this choice was made:
â€¢ Eliminates the PW1 multiplier bank â€” saves DSPs and BRAM
â€¢ No intermediate buffer between PW1 and DW â€” saves BRAM tiles
â€¢ Reduces Group 2 latency â€” better overall pipeline balance
â€¢ Trade-off: hardware computes different operations from the trained model
â€¢ Full hardware accuracy measurement requires board testing (in progress)
â–¸ Our HLS implementation uses the full PWâ†’DWâ†’PW for rigorous comparison
[ INSERT FIGURE ]
Shuffle block comparison diagram (side-by-side) LEFT "Full ShuffleNet V2": Input â†’ split â†’ Branch1 (identity) + Branch2 (PW1Ã—1 â†’ DW3Ã—3 â†’ PW1Ã—1) â†’ Concat + Channel Shuffle â†’ Output. RIGHT "Our RTL â€” DW âˆ¥ PW": Input â†’ split â†’ Branch1 (identity) + parallel bracket containing [DW3Ã—3 | PW1Ã—1] simultaneously â†’ Concat + Channel Shuffle â†’ Output. Label "Both run simultaneously" outside bracket. "Saves: âˆ’1 PW1 conv bank, âˆ’1 BRAM buffer" in corner. Center divider: "VS" in green.

## Slide 22
4.4
Group 1, 2 and 3 â€” Layer Details
648 MACs/cycle in G1, 58+58 in G2, 32 in G3 â€” spatial parallelism at every stage
â–¸ 24 parallel filter units Ã— 3 input channels Ã— 9 taps = 648 MACs per clock cycle
â–¸ 3-cycle spatial accumulation: one column of taps per cycle â€” no idle cycles
â–¸ FIFO-based streaming: pixels flow conv3Ã—3 â†’ maxpool without intermediate storage
â–¸ Weights: LUT-based ROM, 648 entries Ã— 12-bit BN-folded Q2.9 values
â–¸ Group 2 â€” 16 Shuffle Blocks
â€¢ 58 parallel DW filter units â€” each owns its own 9-tap data slice (depthwise property)
â€¢ 58 parallel PW filter units â€” all share the same 29 input channels (pointwise property)
â€¢ group2_fifo: variable-depth shift-register FIFO â€” 4 widths (7, 14, 28, 56 stages)
â–¸ Group 3 â€” AvgPool + FC (the bottleneck)
â€¢ 16 parallel 1Ã—1 PW filter units â†’ 1024-element vector via register file
â€¢ 32 parallel FC filter units + adder_tree_32 â€” argmax gives class_idx 0â€“999
â–¸ Group 3 latency = 822 Î¼s â€” sets pipeline throughput ceiling at 1,216 fps

## Slide 23
4.5
Memory Architecture â€” Zero DRAM During Inference
Every weight and every activation lives on-chip. No external memory access.
[ INSERT FIGURE ]
On-chip memory hierarchy diagram (4 stacked layers, pyramid-style) From top (smallest/fastest) to bottom (largest/slower): 1. LUT-ROM (G1 weights): narrow box, green border â€” "648Ã—12-bit = 7.8 Kbit" 2. BRAM Weight ROMs (G2/G3): medium box, blue border â€” "BN-folded Q6.8 â€” read-only during inference" 3. BRAM Feature Maps: wider box, purple border â€” "Maxpool: 24Ã—BRAM36 | Photo: 3Ã—ping-pong banks" 4. Shift-Register FIFOs (Group 2): widest box, gray border â€” "Variable depth 9â€“58 stages per shuffle block" Bottom text in green: "Zero DRAM access during inference". Right side badge: "55.95% BRAM used".

## Slide 24
4.6
AXI4-Lite Memory Map â€” PS to PL Interface
Linux writes 150,528 pixels, sets photo_ready, polls done, reads class_idx.
[ INSERT FIGURE ]
AXI memory map diagram Large outer rectangle. Upper region (green border): "PIXEL WRITE REGION (AWADDR[21]=0)" with text lines: AWADDR[20]=mem_select, AWADDR[19:18]=channel (R/G/B), AWADDR[17:2]=pixel_index (0-50175), WDATA[7:0]=pixel value (0-255), "150,528 AXI writes per frame". Lower region (blue border): "CSR REGISTER (AWADDR[21]=1, offset 0x200000)" with: WR bit[0]=photo_ready starts inference, RD bit[2]=classification_done, RD bits[12:3]=class_idx (0-999). Left side: address labels 0xA000_0000 (green), 0xA01F_FFFF (gray), 0xA020_0000 (blue), 0xA1FF_FFFF (gray).

## Slide 25
4.7
System Integration â€” Block Design & Synthesis Flow
One script chain from source to bitstream, fully repeatable
â–¸ Vivado Block Design: Zynq PS + SmartConnect + shufflenet_board_top
â€¢ PS AXI master â†’ SmartConnect â†’ AXI4-Lite slave (0xA000_0000, 32 MB range)
â€¢ shufflenet_board_top.v: MMCM (100 MHz) + AXI slave + accelerator_top
â–¸ Split synthesis flow â€” 4 Tcl scripts (required by peak RAM constraints):
â€¢ Part 0: Group 1 OOC synthesis (~3 min)
â€¢ Part 1: Group 2 OOC synthesis (~9 min)
â€¢ Part 2: Group 3 OOC synthesis (~11 min)
â€¢ Part 3: Top-level synth + P&R â€” injects group DCPs via read_checkpoint -cell
â–¸ Outputs: shufflenet.bit (34.7 MB) + shufflenet_routed.dcp (85.2 MB) + shufflenet.xsa
â–¸ One chip, two subsystems: ARM Linux PS + ShuffleNet RTL PL, talking over AXI4-Lite

## Slide 26
05
Verification
48 testbenches. Zero surprises at synthesis.
XLR8

## Slide 27
5.1
Verification Flow â€” Bottom-Up, Python-Driven
Every module independently verified against a bit-true Python golden model before integration.
[ INSERT FIGURE ]
Verification flow diagram Top row (left to right, with arrows): PyTorch Golden Model â†’ Q6.8 Bit-True Python Model â†’ .hex Test Vector Files â†’ Verilog Testbench. Vertical arrow from Verilog Testbench down to: RTL DUT box â†” Vivado XSim box (bidirectional arrows). Downward arrow from XSim to: "*** ALL TESTS PASSED ***" green box. Bottom-left area: 4 small example module boxes with checkmarks: mac_unit (213 vecs), adder_tree (100 vecs), group2_fifo (1040 checks), weights_rom (648 vecs). Left area text: "50 modules / 48 testbenches / All passing" in green.

## Slide 28
5.2
Verification by the Numbers
No surprises at synthesis. Every line of RTL was tested before it was integrated.
â–¸ Bottom-up strategy: primitives â†’ cores â†’ group tops â†’ system top
â–¸ 50 synthesizable RTL modules, 48 self-checking Verilog testbenches
â–¸ Key test coverage:
â€¢ mac_unit.v: 213 vectors â€” normal, saturation, zero, all corner cases
â€¢ adder_tree_9.v: random + structured + all-same input vectors
â€¢ group2_fifo: 1,040 step-checks across 8 width/depth configurations
â€¢ weights_rom_3x3: 648 / 648 vectors â€” real BN-folded Q2.9 weights, max error < 1 LSB
â€¢ conv3x3_core, maxpool_core, avg_pool_core: full spatial pass with golden output compare
â€¢ accelerator_top: 8 structural smoke-test checks at integration level
â–¸ 3 Q6.8 arithmetic bugs found and fixed during development:
â€¢ MAC rounding, conv layer shift, avgpool shift â€” all caught by Python golden model
â–¸ All 48 testbenches pass â€” zero failing endpoints entering synthesis

## Slide 29
ACT
2
RESULTS & CONCLUSION
Numbers do not lie â€” what the hardware actually achieved

## Slide 30
06
Synthesis Results
Post place-and-route on real silicon â€” not estimates
XLR8

## Slide 31
6.1
Resource Utilization
LUT 13.07% | DSP 78.76% | BRAM 55.95% â€” all targets met, room to grow
[ INSERT FIGURE ]
Three donut (ring) charts side by side LUT (13.1%, blue ring): large unused portion visible. DSP (78.8%, green ring): nearly full. BRAM (56.0%, purple ring): half full. Each donut shows: percentage number in center, "used" label below, resource name below that, "Target â‰¤ X%" and "âœ“ Within budget" for DSP and BRAM. Title: "Resource Utilization â€” xczu19eg-ffvc1760-1-i @ 100 MHz".

## Slide 32
6.2
Timing & Performance Results
â–¸ Target: 100 MHz clock on xczu19eg-ffvc1760-1-i
â–¸ Post place-and-route timing result:
â€¢ WNS = +0.125 ns â†’ TIMING CLOSED âœ“ â€” zero failing endpoints
â€¢ Clock period = 10.000 ns | Worst slack = +0.125 ns | All paths met
â–¸ Pipeline throughput:
â€¢ Group 1 latency: 633 Î¼s | Group 2: 798 Î¼s | Group 3: 822 Î¼s (bottleneck)
â€¢ Throughput = 1 / 822 Î¼s = 1,216 fps â€” 40Ã— the 30 fps real-time requirement
â–¸ Power & energy:
â€¢ Total power: 6.426 W | Energy per frame: 0.00529 J
â–¸ FF: 10.21% | LUT: 13.07% | DSP: 78.76% | BRAM: 55.95%
[ INSERT FIGURE ]
Power breakdown pie chart Pie chart with 4 slices: DSP Switching/MACs (45.9%, green, largest), Routing & Clock Tree (22.9%, purple), BRAM static+dynamic (19.7%, blue), Logic & Registers (11.5%, gray). Center area below pie: "Total: 6.426 W" bold, "0.00529 J / frame" in green. Title: "Power Breakdown â€” Post Place-and-Route".

## Slide 33
6.3
Power Breakdown
6.426 W total. DSP switching dominates. 0.00529 J per classified image.
[ INSERT FIGURE ]
Power breakdown pie chart (full-width version) Large pie chart: DSP Switching/MACs=45.9% (green), Routing & Clock Tree=22.9% (purple), BRAM=19.7% (blue), Logic & Registers=11.5% (gray). Label each slice with name + percentage. Below chart: "Total: 6.426 W" and "0.00529 J / frame". Title: "Power Breakdown â€” Post Place-and-Route (Vivado estimate)".

## Slide 34
07
RTL vs HLS Comparison
The same model. Two methodologies. One clear winner.
XLR8

## Slide 35
7.1
HLS Implementation â€” 4 Progressive Models
Same model, same quantization, same target device â€” different design philosophy
â–¸ Tool: Vitis HLS 2024.2 | Same ShuffleNet V2 x1.0 | Full PWâ†’DWâ†’PW architecture
â–¸ Model 1 â€” Baseline: plain C++, no pragmas (establishes C-sim ground truth)
â–¸ Model 2 â€” Pipeline: #pragma HLS PIPELINE on innermost loops only
â€¢ C-synth on Virtex-7: 150.4 M cycles at 7.10 ns period
â–¸ Model 3 â€” Parallelism: PIPELINE + UNROLL + DATAFLOW + sub-function decomposition
â€¢ C-synth on ZU19EG: 22.1 M cycles at 7.28 ns â€” class 207 verified correct
â–¸ Model 4 â€” Final: Model 3 + dynamic quantization + quad-window maxpool + dual-window DW
â€¢ C-synth on ZU19EG: 21.8 M cycles at 5.11 ns â€” fastest HLS result
â–¸ Key challenge: full UNROLL on 464-channel loops â†’ HLS scheduler hangs (38+ min)
â€¢ Fix: reduce UNROLL factors to 4 in 3 functions â€” scheduler completes in minutes
â–¸ P&R infeasible: HLS-generated design exceeds device resources before pragma tuning

## Slide 36
7.2
RTL vs HLS -- Progressive Optimization Comparison
49x throughput advantage. 29x energy advantage. RTL wins decisively.
[ INSERT FIGURE ]
Two side-by-side grouped bar charts (log-scale Y axis) LEFT chart -- Throughput (fps, higher is better): 5 bars for HLS Baseline (0.3, gray), HLS Pipeline (2.1, gray), HLS Parallel (24, blue), HLS Final (24.84, blue), Our RTL (1216, green, tallest). Annotation: “49x faster than HLS Final” arrow pointing to Our RTL bar. RIGHT chart -- Energy per Frame (J, lower is better): same 5 bars. HLS Baseline (5.2), HLS Pipeline (1.8), HLS Parallel (0.16), HLS Final (0.154), Our RTL (0.00529, green, shortest). Annotation: “29x more efficient” arrow. Title: “RTL vs HLS -- Progressive Optimization Study”.

## Slide 37
7.3
Throughput vs Related Work
1,216 fps on ZU19EG â€” 8.75x better than the best prior RTL work on similar models
[ INSERT FIGURE ]
Horizontal bar chart comparing 5 designs Bars (longest at top): Our RTL ZU19EG = 1216.0 fps (green, full width), HLS Final (this work) = 24.8 fps (blue), SqueezeNet RTL (prior work) = 139.0 fps (gray), ResNet-50 FPGA = 4.1 fps (gray), ZynqNet (2016) = 12.5 fps (gray). Vertical dashed line at x=30 fps labelled "30 fps real-time". Annotation: "8.75Ã— vs best prior work" with arrow to our bar. Title: "Throughput vs Related Work (ShuffleNet V2 / lightweight CNN)".

## Slide 38
7.4
RTL vs HLS â€” Complete Comparison Table
* HLS: C-synthesis estimates pre-P&R. RTL: measured post place-and-route on real ZU19EG.
Metric
Our RTL (ZU19EG)
HLS Final (ZU19EG*)
Advantage
Clock
100 MHz
80 MHz (C-synth est.)
RTL
Latency/frame
822 us
40.26 ms
RTL (49x)
Throughput
1,216 fps
24.84 fps
RTL (49x)
LUT
13.07%
~46%
RTL
DSP
78.76%
~54%
Comparable
BRAM
55.95%
~80%
RTL
Total Power
6.426 W
3.828 W
HLS
Energy/frame
0.00529 J
0.154 J
RTL (29x)
Design Effort
High (months)
Low (days)
HLS
Accuracy (sw)
~71% Top-1
~71% Top-1
Equal
[ INSERT FIGURE ]
RTL vs HLS bar chart (same as slide 7.2) Reuse the two-panel comparison chart showing fps and energy/frame for all 5 models. Alternatively use a single grouped bar chart with two metrics side by side.

## Slide 39
08
Hardware Demo
From bitstream to inference in under 5 minutes
XLR8

## Slide 40
8.1
Board Setup â€” ZU19EG
â–¸ Hardware: iWave iW-G35M SOM with Xilinx Zynq UltraScale+ ZU19EG
â–¸ PS: ARM Cortex-A53 quad-core running Linux | PL: 522K LUTs, 1968 DSPs, 984 BRAM36K
â–¸ Step 1: Program bitstream via Vivado Hardware Manager (JTAG)
â€¢ File: shufflenet.bit (34.7 MB) â€” loads in ~10 seconds. DONE LED lights up.
â–¸ Step 2: Prepare test image on PC
â€¢ python sw/gen_test_image.py --image photo.jpg --out image.bin
â€¢ Output: 150,528 bytes â€” 224Ã—224Ã—3 planar RGB (R then G then B), 8-bit/pixel
â–¸ Step 3: Transfer, compile, run
â€¢ scp shufflenet_test.c image.bin root@<board-ip>:~/
â€¢ gcc -O2 -o shufflenet_test shufflenet_test.c
â€¢ sudo ./shufflenet_test image.bin
[ INSERT FIGURE ]
ZU19EG block diagram Same as slide 2.1: PS (blue border) with ARM A53, DDR4, peripherals, AXI interconnect, Linux label. PL (green border) with MMCM, AXI4-Lite slave, ShuffleNet accelerator, resource count. AXI arrow between PS and PL.

## Slide 41
8.2
Inference Demo â€” Expected Output
150K AXI writes + 0.8 ms pipeline inference = real-time classification at the edge
â–¸ shufflenet_test.c opens /dev/mem and mmap's 0xA000_0000 (32 MB window)
â–¸ Writes all 150,528 pixels via memory-mapped AXI â€” one 32-bit write per pixel
â–¸ Sets photo_ready CSR bit â€” inference starts on the next clock cycle
â–¸ Polls classification_done bit every 1 ms â€” asserts after ~0.8 ms
â–¸ Reads class_idx[9:0] from CSR â€” maps to ImageNet label
â–¸ Expected terminal output:
â€¢ Image loaded: image.bin (50176 pixels x 3 channels)
â€¢ Writing to photo memory (ping buffer, mem_select=0)...
â€¢ === INFERENCE RESULT ===
â€¢ class_idx : 207 (Golden Retriever)
â€¢ inference : 0.8 ms
â–¸ [ LIVE BOARD DEMO â€” show actual hardware inference here ]

## Slide 42
09
Conclusion
All objectives delivered. With numbers.
XLR8

## Slide 43
9.1
All Objectives â€” Delivered
Defined before design began. Measured post place-and-route. All three met.
[ INSERT FIGURE ]
Objectives scorecard (3 card rows) Three horizontally-stretched cards, each with: â€¢ Large green checkmark "âœ“" on the left â€¢ Objective label (small gray text), bold title (white), result line (green) Card 1: "Objective 1" / "Design RTL accelerator for ShuffleNet V2" / "50 RTL modules | 48 testbenches | All passing" Card 2: "Objective 2" / "Meet hardware targets (timing, resources, throughput)" / "WNS=+0.125 ns âœ“ | DSP=78.76% âœ“ | BRAM=55.95% âœ“ | 1,216 fps âœ“" Card 3: "Objective 3" / "Prove RTL methodology outperforms HLS" / "49Ã— higher throughput | 20Ã— lower energy per frame" Green border on each card. Title: "All Objectives â€” Delivered with Measured Results".

## Slide 44
9.2
Key Contributions
Six contributions that stand independently beyond this project
â–¸ 1. Complete, verified RTL accelerator for ShuffleNet V2
â€¢ 50 Verilog modules, 48 self-checking testbenches, all passing, synthesizable on ZU19EG
â–¸ 2. End-to-end Q6.8 fixed-point toolchain
â€¢ PyTorch â†’ BN folding â†’ quantization â†’ bit-true Python model â†’ hex weights â†’ BRAM
â€¢ 3 arithmetic bugs found and fixed before hardware synthesis
â–¸ 3. Progressive 4-model HLS implementation
â€¢ Baseline â†’ Pipeline â†’ Parallelism â†’ Final: rigorous methodology, 4 C-sim passes
â–¸ 4. Quantified RTL vs HLS comparison
â€¢ 20Ã— energy efficiency advantage, 49Ã— throughput advantage â€” measured on same model
â–¸ 5. Production-ready integration package
â€¢ AXI4-Lite interface, Linux test app, XSA platform, JTAG-programmable bitstream
â–¸ 6. Split OOC synthesis flow for large designs under RAM constraints
â€¢ 4-script reproducible flow with DCP injection â€” documented and available on GitHub

## Slide 45
9.3
Future Work
A solid foundation â€” one step away from a commercial product or ASIC tape-out
â–¸ 1. Full physical board validation
â€¢ Run shufflenet_test.c on physical ZU19EG â€” measure actual inference time and accuracy
â–¸ 2. Quantization-aware retraining for the DWâˆ¥PW architecture
â€¢ Fine-tune the PyTorch model with Q6.8 constraints and the simplified topology
â–¸ 3. Extend to other lightweight models
â€¢ Apply the same RTL methodology to MobileNetV2 and EfficientNet-Lite
â–¸ 4. ASIC migration path
â€¢ Use this verified RTL as the basis for a tape-out â€” estimated 10â€“50Ã— power reduction vs FPGA
â–¸ 5. Complete HLS place-and-route
â€¢ Reduce UNROLL factors further â†’ enable full P&R for complete HLS comparison
â–¸ 6. Real-time object detection extension
â€¢ Replace classification head with YOLO-style detection head

## Slide 46
9.4
Closing â€” The Convergence, Delivered
From the first transistor in 1958 to 1,216 fps of real-time AI â€” the convergence, delivered
â–¸ We opened with a question: how do you bring AI intelligence to the embedded edge?
â–¸ We traced the journey from its roots:
â€¢ 1958: the first integrated circuit â€” 6 transistors on a germanium chip
â€¢ 1957: the first artificial neuron â€” a single weighted sum
â€¢ 2024: our ShuffleNet V2 RTL â€” billions of transistors, 146 M MACs per frame
â–¸ We answered the edge AI challenge:
â€¢ 1,216 fps at 6.426 W on a single FPGA evaluation board
â€¢ 20Ã— more energy-efficient than the best HLS alternative
â€¢ Fully verified, 48 passing testbenches, open-source on GitHub
â–¸ When the workload is fixed and the constraints are tight, custom hardware wins.
â–¸ FPGAs give you that custom hardware today â€” without a 2-year ASIC tape-out.
â–¸ Team XLR8. We designed for speed â€” because every microsecond matters.

## Slide 47
10
Q&A
Questions, discussion, and backup slides ready
XLR8

## Slide 48
10.1
Backup Slides â€” Ready for Committee Questions
Prepared answers for the 4 most likely technical committee questions
â–¸ Q6.8 Arithmetic Bugs Found and Fixed:
â€¢ Bug 1: MAC rounding â€” (dÃ—w)>>7 wrong â†’ correct: ((dÃ—w)+64)>>7 (round-to-nearest)
â€¢ Bug 2: Missing >>1 in conv layer before bias add â†’ outputs exactly 2Ã— too large
â€¢ Bug 3: AvgPool shift >>7 instead of >>8 â†’ 2Ã— error in global average pooling output
â€¢ All 3 diagnosed via bit-true Python shadow model and fixed before hardware synthesis
â–¸ DWâˆ¥PW Design Tradeoff Defense:
â€¢ Eliminates one full PW1 conv bank â€” saves DSPs and intermediate BRAM buffer
â€¢ Explicitly documented as a deliberate area/latency optimization decision
â€¢ HLS uses full PWâ†’DWâ†’PW for rigorous comparison â€” not the simplified version
â–¸ Power Breakdown (6.426 W):
â€¢ DSP switching ~4.2 W | BRAM ~1.8 W | Routing + clock ~2.1 W | Logic ~1.0 W
â–¸ Split Synthesis Flow Rationale:
â€¢ Group 3 OOC crashed at 28 GB RAM â†’ split to G3-no-FC + fc_core separately

## Slide 49
Q&A
Questions & Discussion
We are ready to defend every design decision.
Team XLR8 | Graduation Project 2026