## Slide 1: Design and Implementation of a ShuffleNet V2 Accelerator on FPGA Using RTL and HLS
XLR8
Graduation Project Discussion | Faculty of Engineering | Menuofia University
Supervised by: Dr. Tamer Fetouh

## Slide 2
Eureka!
The first-ever transistor.
Bell Labs, 1947
In late June 2026, IBM unveiled the world's first sub-1-nanometer chip technology at the 0.7 nm "nanostack" node, packing nearly 100 billion transistors onto a fingernail-sized chip and extending logic scaling into the angstrom era for AI and high-performance computing.

## Slide 3
Eureka!
The first-ever transistor.
Bell Labs, 1947
In late June 2026, IBM unveiled the world's first sub-1-nanometer chip technology at the 0.7 nm "nanostack" node, packing nearly 100 billion transistors onto a fingernail-sized chip and extending logic scaling into the angstrom era for AI and high-performance computing.

## Slide 4: Design and Implementation of a ShuffleNet V2 Accelerator on FPGA Using RTL and HLS
XLR8
Graduation Project Discussion | Faculty of Engineering | Menuofia University
Supervised by: Dr. Tamer Fetouh

## Slide 5
Presentation Outline
What we will cover today
Act I — Before We Design
1. Reinventing Fire
2. Problem Statement
3. Objectives
4. Related Work
5. AI Model Analysis
Act II — Design and Results
6. Design Mapping
7. RTL Architecture
8. Implementation & FPGA Prototyping
9. Conclusion and Q&A

## Slide 6
01
HISTORICAL CONTEXT
From transistors to intelligence — the journey that made this project necessary
ACT 1

## Slide 7
ACT 1
VLSI + AI:
60 Years of Convergence
▸ 1958 — Jack Kilby invents the IC: 6 transistors on germanium
▸ Moore's Law (1965): transistor count doubles every ~18 months
▸ 2023 — Apple M3: 19 billion transistors on a single chip
▸ 1957 — Rosenblatt's Perceptron: the first artificial neuron
▸ 2012 — AlexNet wins ImageNet with a GPU: the AI breakthrough moment
▸ Today — AI compute demand grows 10× per year; hardware barely keeps up

## Slide 8
02
Problem Statement
Why existing solutions fall short — and what we are solving
ACT 1

## Slide 9
ACT 1
The Unfair Advantage
CPU
GPU
AI Accelerator
Design Philosophy: Few powerful cores, optimized for sequential/control-heavy logic.
Perf/Watt: Low for AI workloads.
Fully general-purpose.
Latency: Low for small ops, poor scaling for large parallel ops
Design Philosophy: Thousands of simple cores (SIMD/SIMT), optimized for parallel throughput
Perf/Watt: Moderate-high
General parallel compute (graphics, AI, HPC, crypto)
Latency: Higher per-op latency, but excellent batched throughput
Design Philosophy: Fixed or reconfigurable data path built specifically for tensor/matrix ops.
Perf/Watt: Highest — this is the core value proposition.
Narrow — tuned to specific model/op types
Latency: Very low, deterministic (critical for real-time/edge — e.g., FPGA inference)

## Slide 10
ACT 1
The Unfair Advantage

## Slide 11
ACT 1
Why Cloud AI Fails at the Edge?
▸ Latency: 50–500 ms round trip — useless for real-time control or robotics
▸ Privacy: raw video leaves the device and travels the internet
▸ Bandwidth: streaming HD to the cloud consumes significant network resources
▸ Reliability: no connectivity = no AI — fails in tunnels, remote sites, factories
▸ Power: a data-center GPU draws 300 W — impossible on a battery or embedded rail

## Slide 12
The Challenge
▸ Real-time image classification at the edge requires < 50 ms latency
▸ ARM Cortex-A53 software inference: hundreds of milliseconds per frame
▸ GPU/cloud solutions: too power-hungry and unavailable at the edge
▸ HLS-generated accelerators: high resource overhead, suboptimal efficiency
ACT 1

## Slide 13
03
Solution Objectives
What we set out to prove — and how we will measure success
ACT 1

## Slide 14
ACT 1
Our Approach
▸ Hand-crafted RTL Verilog for ShuffleNet V2 × 1.0
▸ Q6.8 fixed-point datapath with per-layer width optimization
▸ All weights stored on-chip (no DDR access during inference)
▸ HLS models for quantitative RTL vs. HLS comparison

## Slide 15
ACT 1
Design a custom RTL accelerator for ShuffleNet V2

## Slide 16
ACT 1
Design a custom RTL accelerator for ShuffleNet V2

## Slide 17
ACT 1
Target Hardware Metrics

## Slide 18
ACT 1
RTL VS HLS:
Before the Battle

## Slide 19
ACT 1
RTL VS HLS:
Before the Battle
HLS
Advantages
Faster development
Easier debugging
Faster prototyping
Reusable high-level code
Shorter design cycle
Limitations
Lower hardware efficiency
Higher resource utilization
Less architectural control
Timing optimization is harder
Performance depends on the compiler

## Slide 20
ACT 1
RTL VS HLS:
Before the Battle
Hardware resource utilization
Operating frequency and timing
Power and implementation efficiency
Determine the best approach for edge AI deployment.

## Slide 21
04
Related Work
What others have built — and where the gaps remain
ACT 1

## Slide 22
ACT 1
Common FPGA CNN Acceleration Techniques

## Slide 23
ACT 1
Architectural Tradeoffs in FPGA CNN Accelerator Design
Throughput vs resource
On-chip buffering
Quantization: reduces bitwidth
Dataflow style
Interface bottleneck
Efficient lightweight accelerators remain an active research area.

## Slide 24
ACT 1
Why lightweight CNN models?
Traditional CNNs require extensive computation and high memory usage. Mobile devices demand energy-efficient inference.
Lightweight CNNs reduce computation significantly and maintain competitive accuracy with fewer resources.

## Slide 25
ACT 1
ShuffleNet V2
ShuffleNet V2:
Designed specifically for efficient mobile inference.
Uses channel split and channel shuffle.
Reduces memory access cost.
Balances accuracy and computational efficiency.
Suitable for FPGA and edge AI deployment.

## Slide 26
ACT 1
Research Gap Analysis
FPGA CNN accelerators
Focus on performance only
HLS implementations
Limited hardware optimization
RTL implementations
Longer development time
Lightweight CNN studies
Rare RTL–HLS comparison
“Most research evaluates only one methodology”
This project closes all four gaps simultaneously

## Slide 27
ACT 1
Prior Work VS Our Contribution
 | MobileNet FPGA | HLS Only | ShuffleNet Prior | Our Work
Model | MobileNet V2 | Various | ShuffleNet V1 & V2 | ShuffleNet V2
Methodology | RTL or HLS | HLS Only | HLS Only | RTL + HLS
Channel Shuffle HW | N/A | Partial | Omitted | Full RTL
DW Conv | Optimized | Partial | Tool-Managed | Limited Hand-Optimized
Dynamic Quantization | Static Only | Static Only | Limited | Per-Layer Dynamic

## Slide 28
05
AI Model Analysis
Understanding the neural network before building the hardware
ACT 1

## Slide 29
ACT 1
ShuffleNet V2 Architecture

## Slide 30
ACT 1
ShuffleNet V2 building block

## Slide 31
ACT 1
ShuffleNet V2 computational structure

## Slide 32
ACT 1
Software model development
Pretrained PyTorch Model
BN Folding
Verification on ILSVRC
Quantization
Export (weights, config tables, bitwidth CSV)

## Slide 33
ACT 1
Batch Normalization Folding
Before
After

## Slide 34
ACT 1
Why quantization?
Quantization:
Quantization converts values to fixed-point.
Reduces memory and computation cost.
Improves FPGA resource efficiency.
Enables faster real-time inference.

## Slide 35
ACT 1
Dynamic fixed-point Quantization

## Slide 36
ACT 1
Benefits
Reduced arithmetic complexity.
Higher processing throughput.
Lower power consumption.
Efficient edge AI deployment.

## Slide 37
06
DESIGN MAPPING
Translating math into circuits — the bridge between model and hardware
ACT 2

## Slide 38
The Bridge: From SW to HW
ACT 2

## Slide 39
Input/ Output Interfaces
ACT 2

## Slide 40
▸ Q6.8 fixed-point: 15-bit signed, per-layer width optimization
▸ Group 2: 58-filter DW + 12-parallel PW over 16 accumulation steps
▸ Internal 58×784-word dist. RAM buffer between DW and PW phases
▸ Group 3: full-precision 27-bit PW output, bypasses quantizer
▸ BN parameters folded offline using PyTorch — no run-time normalization
Group 1 Conv
8-bit (pixels)
12-bit
Group 2 DW
10-bit
15-bit
Group 2 PW
12-bit
11-bit
Group 3 PW
12-bit
9-bit
Group 3 FC
9-bit
9-bit
Key Design Decisions
ACT 2

## Slide 41
07
RTL ARCHITECTURE
50 modules. 48 testbenches. One accelerator.
ACT 2

## Slide 42
Top-Level System Architecture
ACT 2

## Slide 43
Internal Architecture & Dataflow
ACT 2

## Slide 44
Group 1: The Initializer
ACT 2

## Slide 45
Group 2: Where All Work Happens
ACT 2

## Slide 46
Group 3: The Final Result is Here
ACT 2

## Slide 47
The Combined Flow
ACT 2
Group 1
3×3 Conv + MaxPool
224×224×3 → 56×56×24
24 DSPs 216 total
→
Group 2
16 Shuffle Blocks
56×56×24 → 7×7×464
58 filters 1218 DSPs
→
Group 3
PW + AvgPool + FC + Argmax
7×7×464 → class_idx
16+32 parallel 464 DSPs

## Slide 48
Group 3: The Final Results are Here
ACT 2
Common Primitives
9
modules
mac_unit, adder_trees, quantizer, FIFOs
Group 1
10
modules
conv3x3, maxpool, photo_mem, ROMs, ctrl
Group 2
14
modules
DW, PW, FIFOs, ROMs, ctrl, top
Group 3
11
modules
PW, avgpool, FC, ROMs, ctrl, top
Mem + AXI + Top Level
4
modules
extra_mem, AXI slave, accel_ctrl, accel_top
✓ 48 / 48 TESTBENCHES PASS — Zero failures
▸ Self-contained: no external hex vector files required
▸ Q6.8 Python model: ~71% Top-1 on 100 ImageNet validation images
▸ BN-fold coefficient error: 7.63×10⁻⁶ (within tolerance)

## Slide 49
FPGA Integration
ACT 2

## Slide 50
08
IMPLEMENTATION &
FPGA PROTOTYPING
Seeing is believing — the accelerator in action
ACT 2

## Slide 51
ACT 2
The $5K Baby

## Slide 52
ACT 2
The Work Moment

## Slide 53
ACT 2
The Test: The Moment of Truth

## Slide 54
ACT 2
The Code Compiled Successfully

## Slide 55
ACT 2
The Code Compiled Successfully

## Slide 56
ACT 2
The Code Compiled Successfully

## Slide 57
ACT 2
The Code Compiled Successfully

## Slide 58
ACT 2
100 MHz
Target Clock
+0.096 ns
WNS (Timing Closed)
78.76%
DSP Utilization
58.69%
BRAM Utilization
14.34%
LUT Utilization
Resource Summary
Resource
Used
Available
Utilization
DSP48E2
1,550
1,968
78.76%
BRAM Tile
550.5
984
55.95%
LUT
68,299
522,720
13.07%
Flip-Flop
15,285
1,045,440
1.46%
✓ Timing closed at 100 MHz | WNS = +0.096 ns | WHS = +0.011 ns | 0 failing endpoints
Board-level performance (fps, latency, power) pending hardware deployment
Implementation Results

## Slide 59
ACT 2
The HLS Methodology
Model 1 Baseline
Sequential No directives
Key: Reference
Model 2 Pipelined
#pragma HLS PIPELINE
Key: Pipelining
Model 3 Parallelism
UNROLL factor 16/32 + PARTITION
Key: Parallelism
Model 4 Final
Pipeline + Parallelism + 7 ns
Key: Combined

## Slide 60
ACT 2
RTL VS HLS: The Battle Results
Metric | HLS | RTL
Top-1 Accuracy | 71% | 71%
Fits on the target chip? | No — needs 257–337% of available DSP/BRAM (over capacity, would not fit as generated) | Yes — fits comfortably: 79% DSP, 59% BRAM
Power draw | Not measurable as generated — design is too large to implement | 6.816 W (real, measured)
Energy per image | Not measurable as generated | 0.0053 J (real, measured)

## Slide 61
ACT 2
09
CONCLUSION
Objectives met. Contributions made. What comes next?

## Slide 62
ACT 2
What We Delivered?
▸ Complete RTL implementation of ShuffleNet V2 — timing closed at 100 MHz
▸ 48 RTL modules, 48 self-checking testbenches — all pass
▸ Q6.8 fixed-point model: ~71% Top-1 accuracy on ImageNet
▸ Four Vitis HLS models for RTL vs HLS comparison on ZU19EG
▸ Program ZU19EG and run end-to-end inference test
▸ Measurement of throughput, latency, and on-chip power
▸ Run HLS models and compile RTL vs HLS table
▸ Full documentation: README, block diagrams, reports

## Slide 63
ACT 2
Key Achievement
Fully custom RTL ShuffleNet V2 accelerator synthesized and timing-closed on ZU19EG at 100 MHz DSP: 78.76% | BRAM: 58.69% | LUT: 14.34% | WNS: +0.096 ns

## Slide 64
ACT 2
What’s Next?
Keep developing the architecture to meet higher standards and get better results.
Track all the related work of people implementing the same project with different metrics.
Publish a scientific paper and join academic competitions.
Seek higher and more complex models to implement.

## Slide 65
ACT 2
Q/A
We are ready to defend our cause.

## Slide 66
Thanks for your Time