## Slide 1
Design and Implementation of a
ShuffleNet Accelerator on FPGA
with RTL and HLS
iWave ZU19EG Development Kit | Zynq UltraScale+ MPSoC | 100 MHz
Ahmed Ahmed Nageeb Ahmed Elbermawy | Yousef Abdulrahman Abdulnabi Abdulrahman
Mohamed Ahmed Roshdy Saad | Basmala Hatem Abdullah Mostafa
2026

## Slide 2
Problem Statement
Why a custom FPGA accelerator?
Design and Implementation of a ShuffleNet Accelerator on FPGA with RTL and HLS
2
The Challenge
▸ Real-time image classification at the edge requires < 50 ms latency
▸ ARM Cortex-A53 software inference: hundreds of milliseconds per frame
▸ GPU/cloud solutions: too power-hungry and unavailable at the edge
▸ HLS-generated accelerators: high resource overhead, suboptimal efficiency
Our Approach
▸ Hand-crafted RTL Verilog for ShuffleNet V2 × 1.0
▸ Q6.8 fixed-point datapath with per-layer width optimization
▸ All weights stored on-chip (no DDR access during inference)
▸ HLS models for quantitative RTL vs. HLS comparison
Target: iWave ZU19EG (Zynq UltraScale+ MPSoC) | xczu19eg-ffvc1760-1-i | 100 MHz PL clock
1,968 DSPs • 984 BRAM Tiles • 522,720 LUTs • AXI4-Lite PS interface

## Slide 3
ShuffleNet V2 Architecture
Three hardware groups, pipelined execution
Design and Implementation of a ShuffleNet Accelerator on FPGA with RTL and HLS
3
Group 1
3×3 Conv + MaxPool
224×224×3 → 56×56×24
24 DSPs 216 total
→
Group 2
16 Shuffle Blocks
56×56×24 → 7×7×464
58 filters 1218 DSPs
→
Group 3
PW + AvgPool + FC + Argmax
7×7×464 → class_idx
16+32 parallel 464 DSPs
5-state pipelined FSM: while G3 classifies image N, G1 loads image N+1
Q6.8 fixed-point throughout • All weights on-chip (no DDR) • AXI4-Lite PS interface

## Slide 4
RTL Implementation
Hand-crafted Verilog for maximum efficiency
Design and Implementation of a ShuffleNet Accelerator on FPGA with RTL and HLS
4
Key Design Decisions
▸ Q6.8 fixed-point: 15-bit signed, per-layer width optimization
▸ Group 2: 58-filter DW + 12-parallel PW over 16 accumulation steps
▸ Internal 58×784-word dist. RAM buffer between DW and PW phases
▸ Group 3: full-precision 27-bit PW output, bypasses quantizer
▸ BN parameters folded offline using PyTorch — no run-time normalization
Per-Layer Datapath Widths
Group 1 Conv
8-bit (pixels)
12-bit
10-bit
Group 2 DW
10-bit
15-bit
12-bit
Group 2 PW
12-bit
11-bit
12-bit
Group 3 PW
12-bit
9-bit
27-bit (full)
Group 3 FC
9-bit
9-bit
9-bit
Split Synthesis Flow — Fits in 16 GB RAM
Each group synthesized as separate OOC checkpoint → merged at implementation G1: ~3 min | G2: ~9 min | G3: ~11 min | Top-level P&R: ~1–3 hours

## Slide 5
Verification
48 self-checking testbenches — all pass
Design and Implementation of a ShuffleNet Accelerator on FPGA with RTL and HLS
5
Common Primitives
9
modules
mac_unit, adder_trees, quantizer, FIFOs
Group 1
10
modules
conv3x3, maxpool, photo_mem, ROMs, ctrl
Group 2
14
modules
DW, PW, FIFOs, ROMs, ctrl, top
Group 3
11
modules
PW, avgpool, FC, ROMs, ctrl, top
Mem + AXI + Top Level
4
modules
extra_mem, AXI slave, accel_ctrl, accel_top
✓ 48 / 48 TESTBENCHES PASS — Zero failures
▸ Self-contained: no external hex vector files required
▸ Q6.8 Python model: ~71% Top-1 on 100 ImageNet validation images
▸ BN-fold coefficient error: 7.63×10⁻⁶ (within tolerance)

## Slide 6
Implementation Results
Post-place-and-route on xczu19eg-ffvc1760-1-i
Design and Implementation of a ShuffleNet Accelerator on FPGA with RTL and HLS
6
100 MHz
Target Clock
+0.125 ns
WNS (Timing Closed)
78.76%
DSP Utilization
55.95%
BRAM Utilization
13.07%
LUT Utilization
Resource Summary
Resource
Used
Available
Utilization
DSP48E2
1,550
1,968
78.76%
BRAM Tile
550.5
984
55.95%
LUT
68,299
522,720
13.07%
Flip-Flop
15,285
1,045,440
1.46%
✓ Timing closed at 100 MHz | WNS = +0.125 ns | WHS = +0.011 ns | 0 failing endpoints
Board-level performance (fps, latency, power) pending hardware deployment

## Slide 7
RTL vs HLS Comparison
Four progressively optimized Vitis HLS models — ZU19EG target
Design and Implementation of a ShuffleNet Accelerator on FPGA with RTL and HLS
7
Model 1 Baseline
Sequential No directives
Key: Reference
Model 2 Pipelined
#pragma HLS PIPELINE
Key: Pipelining
Model 3 Parallelism
UNROLL factor 16/32 + PARTITION
Key: Parallelism
Model 4 Final
Pipeline + Parallelism + 7 ns
Key: Combined
⚠ Models 3 & 4 originally caused Vitis HLS scheduler crashes (fully-unrolled 116×116 MACs)
Fixed by reducing UNROLL factor to 16 (116-ch loops) and 32 (232-ch loops)
Performance comparison (fps, power, latency) pending board-level measurements

## Slide 8
Conclusion & Next Steps
Design and Implementation of a ShuffleNet Accelerator on FPGA with RTL and HLS
8
What We Delivered
▸ Complete RTL implementation of ShuffleNet V2 — timing closed at 100 MHz
▸ 48 RTL modules, 48 self-checking testbenches — all pass
▸ Q6.8 fixed-point model: ~71% Top-1 accuracy on ImageNet
▸ Four Vitis HLS models for RTL vs HLS comparison on ZU19EG
▸ Full documentation: README, block diagrams, reports
Next Steps
▸ Program ZU19EG and run end-to-end inference test
▸ Measure throughput, latency, and on-chip power
▸ Run HLS models and compile RTL vs HLS table
▸ Present final performance comparison results
Key Achievement
Fully custom RTL ShuffleNet V2 accelerator synthesized and timing-closed on ZU19EG at 100 MHz DSP: 78.76% | BRAM: 55.95% | LUT: 13.07% | WNS: +0.125 ns
Ahmed Elbermawy • Yousef Abdulrahman • Mohamed Roshdy • Basmala Mostafa — 2026